## Slide 1: Digital Twin of a Rotating Shaft for Predictive Maintenance using MATLAB Simulink and Simscape
MDM2104 – Case Study: Intelligent Systems in Production
Group 9
Sameer K. Subair
Karthik Gopi
Nihal Sait Nishan
Abdul Rashid Kundladi

## Slide 2: Previous Achievements
Simulink Digital Twin model created
Healthy & faulty shaft simulation done
Torque, angular velocity, & vibration signals extracted
FFT & RMS analysis implemented
Baseline fault signatures identified

## Slide 3: Methodology Overview
1. System Identification:
ML Model 1 learns base shaft parameters from dataset.
2. Simulation:
Simulink generates vibration signals under healthy & faulty conditions.
3. Feature Extraction:
Extract RMS, FFT peaks, crest factor, harmonics, etc.
4. Machine Learning (Phase 1):
Decision Tree used for baseline parameter estimation.
5. Future Work:
Degradation Model + LSTM RUL model + Dashboard.
6. Feedback Loop:
Simulation → Features → Wear update → RUL → Next cycle.

## Slide 4: Complete Digital Twin Workflow
The Digital Twin operates in a continuous loop that emulates real machine operation:
Initialization (Healthy State Setup)
ML Model 1 analyzes historical vibration datasets
Learns optimal base parameters:
Spring = 500 N·m/rad
Damper = 0.50 N·m·s/rad
Inertia = 0.124 kg·m²
Environmental factors initialized (temperature, humidity, dust, environment type)
Historical database initialized
Simulation Cycle (1 cycle = 1 simulated hour)
Run Simulink shaft model using current parameters
Generate vibration signals (torque, velocity, displacement)
Extract 12+ features (RMS, peak, crest factor, FFT peaks, band energies)
Wear Update (Future Phase)
ML Model 2 calculates parameter degradation based on:
Operating conditions
Environmental conditions
Historical vibration trends
Produces updated parameters (e.g., spring stiffness ↓, damping ↑)
RUL Prediction (Future Phase)
ML Model 3 (BiLSTM) reads last 30-day vibration history
Predicts Remaining Useful Life
Stores prediction + updated parameters
Dashboard Update
System visualizes health state, vibration evolution, and predicted RUL
This loop repeats continuously, creating a true real-time digital twin.

## Slide 5: Planned Architecture – Degradation Model
Inputs :
Vibration features from last hour
Environmental conditions
Current shaft parameters
Operation duration
Core Logic :
Regression-based degradation estimation
Example :
Spring decreases 0.05–0.2% per hour
Damper increases based on contamination
Inertia changes due to micro-deformation
Outputs :
Updated spring stiffness
Updated damping coefficient
Updated inertia
Wear state saved

## Slide 6: Planned Architecture – LSTM RUL Model
Input:
30-day vibration feature history
Sequential time-series data
Neural Network:
BiLSTM (128 units)
Dropout (0.3)
Dense layer
Regression output
Output:
Predicted RUL
Prediction confidence
Progressive degradation trend

## Slide 7: Kaggle Dataset
Dataset: Vibration Analysis on Rotating Shaft (Kaggle)
https://www.kaggle.com/datasets/jishnukoliyadan/vibration-analysis-on-rotating-shaft
Contains vibration data under:
Healthy shaft
Misalignment
Unbalance
Bent shaft
Bearing faults
Data Type:
Accelerometer vibration signals (time-series)

## Slide 8: Data Preprocessing
Performed the following:
Imported vibration CSV files
Filtered high-frequency noise
Segmented data into windows
Normalized each window
Labeled signals (healthy vs fault type)

## Slide 9: Feature Extraction
Extracted the following from each window:
Time-Domain Features
RMS
Peak-to-peak
Crest factor
Kurtosis
Frequency-Domain Features
FFT dominant peak
Harmonics
Spectral band energy
These features are used for ML training

## Slide 10: Machine Learning Model
Implemented Decision Tree Classifier as first ML model.
Steps Completed:
Combined features from Simulink + Kaggle
Split into train/test sets
Trained baseline Decision Tree
Performed classification of faults
Output:
Model successfully identifies basic fault patterns
Serves as baseline for future deep learning models

## Slide 11: Results of ML Model
Decision Tree trained on extracted features
Successfully classified healthy vs faulty samples
Provided first baseline accuracy
Identified need for more advanced sequence models (later phase)

## Slide 12: Summary of Work Completed
Dataset integrated
Preprocessing completed
Feature extraction completed
Healthy–faulty comparison validated
Baseline ML model implemented
Feature matrix generated for next phase

## Slide 13: Future Goals
Implement Degradation Model (ML Model 2)
Develop LSTM-Based RUL Prediction Model (ML Model 3)
Integrate Digital Twin with ML Models
Build Interactive Dashboard
Full End-to-End Predictive Maintenance Digital Twin